## Slide 1: Using Structured Failure Data for Reasoning of Failure Causes and Analysis of Factors Influencing Failure
AVIC China Aero-Polytechnology Establishment
Dec. 18, 2019

## Slide 2: Report contents
1. Reasoning of failure causes
2. Analysis of factors influencing failure

## Slide 3: Technical proposal
Reasoning of failure causes using structured failure data
Ground wire screw is fractured
Sensor’s copper tube is damaged
Adjust the heating element’s power distribution
Change the sensor model
Replace the shell assembly
Replace the screw
Replace the copper tube
Pilot/static tightness inspection reveals the leakage
Pilot/static tube leaks
Airspeed indicator is too high/too low
Shell assembly has structural damage
Sensor is broken
Airspeed indicator stops/displays nothing
The temperature is too high to be tolerated by the ferromagnetic fluid

## Slide 4: Technical proposal
Reasoning of failure causes using structured failure data
布尔
Input the training data
Extract key features and failure causes
Delete records with missing features
Boolean coding of textual features
Calculate the time intervals for date data
Feature normalization
Build a k-nearest neighbor model
Select model parameters
Model training
Input the test set
Failure cause prediction
Output the results

## Slide 5: Technical proposal
Reasoning of failure causes using structured failure data
Date of failure | User type | Delivery date of faulty part | Working time of faulty part | Main fault symptom | Working calendar time
20190516 | China Southern Airlines | April 1, 2015 | 204:58 | Airspeed indicator is too high/too low | 1506
Reasoning
Timing: Quarter
User type: Airline
Working time: hours (h)
Working calendar time: hours (h)
Fault symptom: text description
Feature extraction from entity attributes
Failure cause/remedial action and probability
Replace the rotary transformer
Add a buffer structure to separate the bevel gear from limit bushing
Adjust the heating element’s power distribution
0.42
0.30
0.28
Sensor’s static vent is blocked
The temperature is too high to be tolerated by the ferromagnetic fluid
Bevel gear rotates relative to the shaft
Out-of-tolerance deviation in angle of attack
Probability
故障原因
Failure cause

## Slide 6: Technical proposal
Analysis of factors influencing failure using structured failure data
The delivery dates of 57% of the sensors are concentrated in the range from 2012 to 2013; and 70% of sensors have working times of between 250-650 h.
The delivery dates of 75% of the sensors fall within two ranges: from the 2nd quarter of 2005 to the 1st quarter of 2006 and from 2009 to 2010; the working times of 70% of the sensors are concentrated in the range of 1000-1500 h.
Working times of all sensors are less than 35 h, which is characteristic of early failure.
Reasons behind the concentration of delivery rates can be examined from the perspectives of batch manufacturing, batch delivery to users, etc. Reasons behind the concentration of working times can be analyzed in terms of design, materials, stress in specific operating conditions, etc.
Delivery date
Delivery date
Delivery date
Delivery date
Failure statistics of sensors whose failure mode is “Corrosion”
Failure statistics of sensors whose failure mode is ‘Sideslip angle does not follow’
工作时次
工作时次
工作时次
工作时次
Working time
Working time
Failure statistics of sensors whose failure mode is “Stuck”
Working time
Working time
Working time
The delivery dates of 40% of the sensors are between the second half of 2011 and the first half of 2012; 60% of the sensors have working times less than 250 h.
Failure statistics of sensors whose failure mode is “Heating failure”

## Slide 7: Thanks for listening!